## Slide 1: Diffusion MRI Analysis
Sonia Pujol, Ph.D.
Surgical Planning Laboratory
Harvard University

## Slide 2: Brain Anatomy
White matter ~45% of the brain
Myelinated nerve fibers
(~ 10 μm axon diameter)
Diffusion MRI Analysis

## Slide 3: White Matter Exploration
First non-invasive window on the organization of brain white matter pathways in-vivo
Diffusion MRI Analysis

## Slide 4: Tutorial Outline
This tutorial is an introduction to the fundamentals of Diffusion MRI analysis, from the estimation of diffusion tensors to the interactive 3D visualization of fiber tracts.
Diffusion MRI Analysis

## Slide 5: Tutorial Dataset
The tutorial dataset DiffusionMRI_tutorialData is a Diffusion Weighted MR scan of the brain acquired with 41 gradient directions and one baseline.
Diffusion Sensitizing Gradients
Diffusion Weighted Images
Diffusion MRI Analysis

## Slide 6: Tutorial Software
The tutorial uses the 3DSlicer version 4.3
software available at www.slicer.org
Disclaimer
It is the responsibility of the user of 3DSlicer to comply with both the terms of the license and with the applicable laws, regulations and rules. Slicer is a tool for research, and is not FDA approved.
Diffusion MRI Analysis

## Slide 7: 3DSlicer software
An end-user application for image analysis
An open-source environment for software development
A software platform that is both easy to use for clinical researchers and easy to extend for programmers
3D Slicer is a multi-institution effort supported by the National Institutes of Health.
Diffusion MRI Analysis

## Slide 8: Learning Objectives
Following this tutorial, you’ll be able to
1) Estimate a tensor volume from a set of Diffusion Weighted Images
2) Reconstruct DTI tracts from a pre-defined region of interest
3) Interactively visualize DTI tracts seeded from a fiducial
Diffusion MRI Analysis

## Slide 9: MR Diffusion Analysis Pipeline
DWI Acquisition
Tensor Calculation
Scalar Maps
3D Visualization
Diffusion MRI Analysis

## Slide 10: Part 1: From DWI images to Tensors
Diffusion MRI Analysis

## Slide 11: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
First, start Slicer4

## Slide 12: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
In your files archive, locate the file dwi.nhdr in the dataset folder for this tutorial

## Slide 13: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Drag and drop the file dwi.nhdr onto the viewer of the Slicer4 application

## Slide 14: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Exit the archive folders window, and click OK to load the dataset to Slicer

## Slide 15: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Slicer displays DWI volume of the brain

## Slide 16: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Modules menu and select the module Volumes

## Slide 17: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Adjust the Window Level editor presets with the Volume module menu

## Slide 18: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position your mouse over the pin icon, then click on the link icon and the fit image to window icon

## Slide 19: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Slicer layout menu and select the Red slice only layout

## Slide 20: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Slicer displays only the Axial anatomical slice in the Viewer

## Slide 21
Estimation of the tensors from diffusion weighted image
from DWI to DTI

## Slide 22: Exploring the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Modules menu and select the module DWI to DTI Estimation

## Slide 23: Exploring the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module DWI to DTI Estimation in the modules menu:
-select the Input DWI volume ‘dwi’
-select Output DTI Volume ‘Create and Rename New Volume’, and rename it ‘dti’
-select Output Baseline Volume ‘Create and Rename new Volume’, and rename it ‘baseline’
-select the Estimation Parameter ‘WLS’ (Weighted Least Squares) and click on Apply.

## Slide 24: Exploring the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position your mouse over the pin icon and select the volume dti

## Slide 25: Exploring the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Slicer displays the DTI volume in color by orientation mode:
Red: right-left
Green: anterior-posterior
Blue: inferior-superior

## Slide 26: Exploring the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Use the slider to browse through the dti volume, and try to locate the Corpus Callosum

## Slide 27: Corpus Callosum
The corpus callosum is a broad thick bundle of dense myelinated fibers that connect the left and right hemisphere. It is the largest white matter structure in the brain
Image from Gray’s Anatomy
Diffusion MRI Analysis

## Slide 28: Corpus Callosum
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Corpus Callosum

## Slide 29
Scalar measurements of diffusion tensor
from DTI to FA

## Slide 30: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Modules menu and select the module Diffusion Tensor Scalar Measurements

## Slide 31: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Fill in the following information:
-Set Input DTI Volume to ‘dti’
-Select Output Scalar Volume ‘Create new Volume’ and rename it ‘fa’
-Select the Operation ‘Fractional Anisotropy’
-Click on Apply to calculate the Fractional Anisotropy map of the tensor volume

## Slide 32: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
The FA image appears in the red viewer

## Slide 33: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Slicer layout menu and select Conventional layout

## Slide 34: Part 2: Tractography
Diffusion MRI Analysis

## Slide 35
Tractography seeded from
a region of interest (ROI)

## Slide 36: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position your mouse over the pin icon, click on << icon and change the Foreground to ‘None’ and the background to ‘fa’

## Slide 37: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module Editor

## Slide 38: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select Apply when the ‘label-map window’ appears,
then switch to the Yellow slice only layout

## Slide 39: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the fit to screen icon to adjust the dimensions of the yellow slice viewer to fit the screen

## Slide 40: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the DrawEffect tool

## Slide 41: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Outline the contour of the Corpus Callosum with the DrawEffect tool equipped and press enter. Repeat this step with 3 adjacent sagittal slices

## Slide 42: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
The tracts will be seeded from the region of interest (ROI) defined in the Corpus Callosum area.

## Slide 43: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module Tractography Label Map Seeding

## Slide 44: Labelmap Seeding: I/O
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
-Set the Input DTI Volume to ‘dti’
-Set the Input Label Map to ‘fa-label’
-Set Output Fiber Bundle to ‘Create and Rename New Fiber Bundle’ and rename it ‘corpusCallosum’

## Slide 45: ROI Drawing
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Under Seed Placement Options, check off the option for ‘Use Index Space’

## Slide 46: Labelmap Seeding: parameters
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the default Tractography Seeding parameters:
-Minimum Path Length: 10 mm
-Maximum Length: 800 mm
-Stopping Criteria: FractionalAnistropy
-Stopping Value: 0.15
-Stopping Track Curvature: 0.8
-Integration Step Length: 0.5 mm
Click on Apply

## Slide 47: Labelmap Seeding: Tracts
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
The tracts generated in the corpus callosum area appear in the 3D viewer.

## Slide 48: Tractography Results
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position the mouse over the pin icon and click on the eye icon to display the axial slice in the 3D viewer

## Slide 49
Tractography seeded from a fiducial

## Slide 50: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module Mark Ups

## Slide 51: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the arrow icon to create a fiducial

## Slide 52: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position the fiducial in the left cingulum of the coronal slice

## Slide 53: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Double click on the fiducial and change the name to LeftCingulum

## Slide 54: Fiducial Seeding
Diffusion MRI Analysis
Select the module Tractography Interactive Seeding
Select the Input DTI volume ‘dti’
Select the Input Fiducials, Model or Label Map ‘F’
Select the Output Fiber Bundle ‘Create New Fiber Bundle’ and rename it ‘Cingulum’

## Slide 55: Fiducial Seeding
Diffusion MRI Analysis
Set the tractography parameters as follows:
-Fiducial region size: 2.5 mm
-Fiducial Seeding Step Size: 1.0 mm
-Maximum number of seeds: 100
-Minimum Path Length: 10 mm
-Maximum Path Length: 800 mm
-Stopping Criteria: Fractional Anisotropy
-Stopping Value: 0.15
-Stopping Track Curvature: 0.8
-Integration step length: 0.5 mm
-Create Tracts Initially as Tubes

## Slide 56: Fiducial Seeding
Diffusion MRI Analysis
Part of the left cingulum appears in the 3D viewer.
Move the Left Cingulum fiducial to explore the spatial relationship between the left cingulum and the corpus callosum

## Slide 57: Fiducial Seeding
Diffusion MRI Analysis
Go to the Markups module

## Slide 58: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the arrow icon to create a second fiducial

## Slide 59: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position the fiducial in the right cingulum of the coronal slice

## Slide 60: Fiducial Seeding
Diffusion MRI Analysis
Double click on the Name and change it to RightCingulum

## Slide 61: Fiducial Seeding
Diffusion MRI Analysis
Part of the left and right cingulum appear in the 3D viewer.
Move the fiducials to explore the spatial relationship between the left and right cingulum, and the corpus callosum

## Slide 62: Fiducial Seeding
Diffusion MRI Analysis
Click on the arrow icon to create a new fiducial, and position it in the 3D viewer

## Slide 63: Fiducial Seeding
Diffusion MRI Analysis
Move the fiducial F-3 in the 3D viewer to explore the dti dataset

## Slide 64: Tractography ‘on-the-fly’
Diffusion MRI Analysis
The Fiducial Seeding functionality allows you to do tractography ‘on-the-fly’ to explore white matter structures interactively

## Slide 65: DTI Analysis
Diffusion MRI Analysis
Select the module Data to display the list of elements that have been generated in this tutorial

## Slide 66: Conclusion
This tutorial guided you through the different steps of a Diffusion MR Analysis pipeline, from tensor estimation to 3D tracts visualization, for exploring and studying the brain white matter pathways.
Diffusion MRI Analysis – Sonia Pujol, Ph.D.
NA-MIC ARR 2012

## Slide 67
Contact: spujol@bwh.harvard.edu
Diffusion MRI Analysis – Sonia Pujol, Ph.D.
NA-MIC ARR 2012

## Slide 68: Slicer Community
www.slicer.org
Mailing lists:
slicer-user@bwh.harvard.edu
slicer-devel@bwh.harvard.edu
Diffusion MRI Analysis – Sonia Pujol, Ph.D.
NA-MIC ARR 2012

## Slide 69: Acknowledgments
Diffusion MRI Analysis
National Alliance for Medical Image Computing (NA-MIC)
NIH U54EB005149
Neuroimage Analysis Center (NAC)
NIH P41RR013218
Parth Amin, WIT ’16
Matthew Flynn, WIT ‘16