## Slide 1: Slicer QIICR The Relevant Parts of DICOM
David Clunie
PixelMed Publishing

## Slide 2: DICOM needs for Specific Aims
SA1: “Workflows and tools for analyzing longitudinal imaging and derived data. Multiparametric prostate MRI, PET/CT of head & neck cancers, and MRI of microvascular properties of glioblastomas are projects in QIN that will be analyzed to define core requirements for functionality and internal organization. Custom analysis and data organization workflows will be designed within 3D Slicer for each of the clinical projects.”

## Slide 3: DICOM needs for Specific Aims
SA2: “Standards-based structured reporting and representation of quantitative analysis results. The internal organization of the software developed in SA1 will be analyzed and mapped into interoperable format according to the DICOM standard compatible with commodity PACS technology. The developed functionality will be used to store and share the results of analyses produced by the clinical projects.”

## Slide 4: DICOM needs for Specific Aims
SA3: “User- and developer-level interfaces to data archives. Interoperability of data objects defined in SA2 with locally installed and national data archives for cancer imaging research will be established. User-level interfaces will be created in 3D Slicer to interface data archives, such as The Cancer Image Archive (TCIA).”

## Slide 5: DICOM needs – why?
Compatible with commodity PACS
Store and share the results of analyses
Interoperability of data objects

## Slide 6: DICOM needs – what?
Longitudinal imaging
Derived data
Multi-parametric data
Micro-vascular properties (DCE-MR)
Structured reporting
Quantitative analysis results

## Slide 7: DICOM versus NRRD etc.
DICOM objects contain “composite context”
  Patient … same for all instances for patient
  Study … same for all instances for procedure
  Series … new for each derivation
  Equipment
  Frame of Reference
Needs to be de-identified or access restricted

## Slide 8: DICOM versus NRRD etc.
DICOM objects contain “composite context”
  Patient … same for all instances for patient
  Study … same for all instances for procedure
  Series … new for each derivation
  Equipment
  Frame of Reference
Needs to be de-identified or access restricted
Slicer needs to preserve and propagate
  into derived objects (images, SEG, REG, SR etc.)

## Slide 9: DICOM for Imaging in General
Slicer supports import sets of slices
“map from acquisition data organization into volume representation” [Slicer wiki]
Slicer cannot export back to DICOM
Import supports only single-frame (legacy) rather than “enhanced multi-frame” DICOM CT and MR objects

## Slide 10: DICOM for Imaging in General
Slicer supports import sets of slices
“map from acquisition data organization into volume representation” [Slicer wiki]
Slicer cannot export back to DICOM
Import supports only single-frame (legacy) rather than “enhanced multi-frame” DICOM CT and MR objects
Extend slicer to import DICOM Enh.MF
Extend slicer to export DICOM SF and Enh.MF

## Slide 11: Enhanced Multi-Frame
More like NRRD (etc.) volume in one “file”
All slices in single DICOM Instance
“Vector” of attributes describing each frame
Attributes grouped with similar siblings
  “functional groups”
Itemized per-frame
  Per-Frame Functional Groups Sequence
  same order as encoded frames in Pixel Data
Commonality factored out
  Shared Functional Groups Sequence

## Slide 12: Multi-frame Functional Groups
Per-frame attributes
Pixel data
Shared attributes

## Slide 13: Slicer & DICOM Import/Export
Map geometry and acquisition timing
Internal Slicer representation
External DICOM SF and Enh.MF modes
+/- DICOM Stacks (helpful, easy)
+/- DICOM Dimensions (required for SEGs)
Single 3D volume
4D volumes
Round-trip fidelity if same Frame of Reference

## Slide 14: Slicer & DICOM Import/Export
Map geometry and acquisition timing
Internal Slicer representation
External DICOM SF and Enh.MF modes
+/- DICOM Stacks (helpful, easy)
+/- DICOM Dimensions (required for SEGs)
Single 3D volume – definitely in Slicer
4D volumes – needed for perfusion (DCE-MR)
Round-trip fidelity if same Frame of Reference

## Slide 15: DICOM for Longitudinal Imaging
Cross-procedure timing (year/month/day)
  within-procedure timing – contrast/radionuclide
All existing DICOM image objects contain
  dates & times (study/series/acquisition/content)
  reference to local or explicit time zone
Possibility of named/ordinal time points
  Clinical Trials Modules (optional) (composite ctx.)
  esp. Clinical Trial Time Point
  or could manage “out of band” (store elsewhere)

## Slide 16: DICOM for Longitudinal Imaging
Cross-procedure timing (year/month/day)
  within-procedure timing – contrast/radionuclide
All existing DICOM image objects contain
  dates & times (study/series/acquisition/content)
  reference to local or explicit time zone
Possibility of named/ordinal time points
  Clinical Trials Modules (optional) (composite ctx.)
  esp. Clinical Trial Time Point – add to Slicer
  or could manage “out of band” (store elsewhere)

## Slide 17: DICOM for Derived Data
Derived data that is image or image like
Pixel (voxel) rather than ROI-based calculation
Intermediate calculations on images
“Parametric maps”
e.g., DCE-MR Ktrans, PET SUVbw, CT RCBV
Each pixel (voxel) has real world meaning
  continuous value, dimensionless, physical units
Representation – float or scaled integer?

## Slide 18: DICOM for Parametric Maps
Which IOD (SOP Class)?
  same as original modality (CT, MR)
  secondary capture
  something new ? private, extend standard
  can be multi-frame rather than single frame
  give user a choice (based on their tools)
What encoding?
  scaled integers – everybody supports
  floating point – not yet standard; but can work
Easy to make
  if geometry & composite context available to propagate

## Slide 19: DICOM for Parametric Maps
Which IOD (SOP Class)?
  same as original modality (CT, MR)
  secondary capture
  something new ? private, extend standard
  can be multi-frame rather than single frame
  give user a choice (based on their tools)
What encoding? Slicer should support both
  scaled integers – everybody supports
  floating point – not yet standard; but can work
Easy to make
  if geometry & composite context available to propagate

## Slide 20: DICOM for Label Maps
Which IOD (SOP Class)?
  Image
  Segmentation
What encoding?
  Image
    PALETTE COLOR (each pixel is index into RGB LUTs)
    no semantics for value
  Segmentation
    each frame is a “segment” (one label)
    each pixel (voxel) can be binary or occupancy fraction/probability
    segment is described with coded property category/type/anatomy

## Slide 21: DICOM for Label Maps
Which IOD (SOP Class)?
  Image
  Segmentation
What encoding?
  Image – Slicer could support
    PALETTE COLOR (each pixel is index into RGB LUTs)
    no semantics for value – could extend standard to add properties
  Segmentation – Slicer should definitely support
    each frame is a “segment” (one label)
    each pixel (voxel) can be binary or occupancy fraction/probability
    segment is described with coded property category/type/anatomy

## Slide 22: Segmentation Possibilities
Simple encoding of single ROI (segment) on one or more spatial slices (e.g., 3D tumor)
Different tissue types in one lesion (e.g., necrotic part, solid part, enhancing part)
Multiple lesions in one object, each a separate segment
An entire classification of tissues in a volume (e.g., brain atlas)

## Slide 23: Segmentation Possibilities
Simple encoding of single ROI (segment) on one or more spatial slices (e.g., 3D tumor)
Different tissue types in one lesion (e.g., necrotic part, solid part, enhancing part)
Multiple lesions in one object, each a separate segment
An entire classification of tissues in a volume (e.g., brain atlas)
Slicer should support all that it can create

## Slide 24: Harvard SPL Brain Atlas
Took NRRD files
  converted LUT indices to codes
  for each slice of LUT indices, made a binary frame of each index
Resulting SEG object
  315 segments, 6463 frames
Not a very efficient representation
  sparse, so compresses very well (zip 71:1)
  sacrificing space allows overlapping segments

## Slide 25: Harvard SPL Brain Atlas

## Slide 26: DICOM for Quantitative Results
Parametric maps are one quantitative result
Need to encode Regions of Interest (ROIs)
Applied to original images & parametric maps
Where is the ROI?
  contours or segments
  2D (image-referenced) or 3D (frame of reference)
What is (are) the resulting calculations(s)?
  type, value, units

## Slide 27: DICOM Encoding of ROIs
Private elements (evil & must be stopped)
Curves in image (weak semantics, old, retired)
Overlays in image (weak semantics)
Presentation States (weak semantics, PACS favorite)
Structured Reports (best choice, more work)
RT Structure Sets (coordinates only)
Segmentations (per-voxel ROIs; use with SR)

## Slide 28: DICOM Encoding of ROIs
Private elements – Not relevant to Slicer
Curves in image – Not relevant to Slicer
Overlays in image – ?? Slicer Export
Presentation States – ?? Slicer Export since PACS favorite
Structured Reports – Slicer Import/Export
RT Structure Sets – Slicer Import/Export
Segmentations – Slicer Import/Export

## Slide 29: DICOM Structured Reports
Hierarchical structure
  codes, numbers, coordinates, image references, etc.
Flexibility is constrained by templates
  just as XML is constrained by DTD or Schema
Standard DICOM binary representation
  easily stored in PACS though visualization remains challenging
  easily transcoded to XML for processing
Widely used in existing quantitative modalities
  echo-cardiography, obstetric ultrasound

## Slide 30: SR – Questions & Answers
Basic structure is name-value pair
  name is the “question” (code)
  value is the “answer” (text, code, numeric, etc.)
Different style choices possible, e.g.
  (M-54000,SRT,“Necrosis”) = (G-A203,SRT,“Present”)
  (F-00005,SRT,“Finding”) = (M-54000,SRT,“Necrosis”)
Template of questions & value sets
  populated by human (pick lists from value sets)
  encode image processing results (e.g., detect signal)
  rule based (e.g., too small to measure)

## Slide 31: DICOM SR – details inside

## Slide 32: DICOM SR – as visualized
Date | Volume | Auto LD | Auto SD
20021207 | 27080 | 49 | 27
… | … | … | …
Ref. to SEG

## Slide 33: DICOM RT Structure Sets
Simple structure
  focus: iso-contour 3D coordinates regions to treat/spare
  very limited semantics
  no standard/extensible measurements, just volume
Standard DICOM binary representation
  easily transcoded to other DICOM objects like SR or PS if 3D (patient-relative) to 2D (image-relative) coordinate mapping is available (e.g., via source images or an SR image library)
Widely used in existing RT & non-RT workstations
  also understood by many academic software tools

## Slide 34: DICOM Presentation States
Intended to preserve appearance
  grayscale pipeline (window)
  spatial transformation (pan/zoom)
  annotation (text, overlays, vector graphics)
Lack semantics
  what does text “mean”?
  which graphic is it associated with?
Overall, a poor choice for quantitation
  may be all that is available in many PACS (to create/view)

## Slide 35: Show Your Work
Save/restore state +/- undo/repeat
Intermediate images
  floating point, propagation of composite context
Description of steps
  codes in SR templates
Are other common artifacts that aren’t images
  Registration objects (REG)
  Real World Value Maps (RWVM)
  Fiducials
  Surfaces (Surface SEG)

## Slide 36: DICOM Registration & Fiducials
Mapping between 3D coordinates
  DICOM Registration – rigid matrix
  DICOM Deformable Registration
Location of specific points
  DICOM Fiducial
Used to save manual or automated results
  save application state for further work later
  re-use for other purposes (e.g., sync’d scrolling)

## Slide 37: DICOM Real World Value Maps
Separate pipelines based on pixels
  what to show on the display
  what the pixel (voxel) “means”
e.g., MR pixel values
  signal intensity windowed for display
  mapped to physical unit (e.g. velocity for phase contrast)
DICOM implementation
  within image or separate object (e.g., derived later)
  linear equation or LUT, applied to all or sub-set of range
  point operation (all voxels) (unlike US Region Calibration)

## Slide 38: Real World Value Maps

## Slide 39: Putting it all together …
Analysis Workstation
Current DICOM Images from Modality
DICOM Segmentation
DICOM Registration
DICOM SR
DICOM Real World Value
DICOM Parametric Map Images
PACS Store, Distribute and Review
Previous DICOM Images from PACS
Previous DICOM SR etc

## Slide 40: Lessons from Commercial Example
Siemens syngo.Via MultiModality Oncology
REG, RWVM (PET SUV calculation), SEG
SR with measurements, co-ords & references
Encoding changes as concept of template & standard support is improved (3D coords)
Bugs … bit order in SEG for table removal
Need to support old “versions” of templates
Avowed goal is save/restore state only

## Slide 41: Toolkit support
DICOM network (send/receive/query/retrieve)
DICOM parsing (nested lists of attribute)
DICOM <-> XML conversion
Extraction of “models” (classes?) of content
  image extraction (8/16/32 bit, gray or RGB)
    compression/decompression (codecs)
  structured report “content tree”
  enhanced multi-frame concepts (esp. SEG)
    geometry – spacing, orientation, position
    dimensions, stacks, timing
Coded content (SNOMED, LOINC, RadLex, FMA)

## Slide 42: Gaps in DICOM Standard
Floating point pixel data
  existing objects scaled integers only
  do have OF and OD data types
  use with “private” objects
  PixelData (7FE0,0010) with OF or OD
    works, but problem with big/little endian conversions
  new “Floating” PixelData (7FE0, ????)
    a bit more work for all toolkits, but probably safer
  need convincing (low risk) “use case” for committee acceptance

## Slide 43: Selected Tools
Slicer, CTK, dcmtk
dcmtk – good SR, XML support, no enhanced multi-frame or geometry abstractions, excellent network, compression, security support
CTK –widgets using (most recent ?) dcmtk ??
Slicer – dcmtk and ITK geometry handling (need gap analysis re. multi-frame geometry translations)
? handling of abstractions like extracting 3D/4D/nD volume data set from mixed series, etc. (“frameset” “partitioning” problem)

## Slide 44: Archival Aspects – Legacy Images
Well supported in existing open image archives (OAIs) (or generic OTS/COTS DICOM archives/VNAs)
Ingestion – file import, C-STORE SCP, web submit (+/- de-identification)
Indexing – parse DICOM “header” and extract patient(subject)/study/series/image values
Query – search using extracted header values – C-FIND SCP, web page, web services (SOAP or RESTful)
Retrieve – C-MOVE (C-GET less common), web page (immediate or shopping cart), web services (SOAP or RESTful)

## Slide 45: Archival Aspects – Other Objects
More recent image objects
  enhanced CT/MR – ?? Indexing/query limitations
SEGs, RWVMs, REGs, SRs
  indexed like images – retrievable (esp. whole study)
  no specific query support
  no “structured querying of analysis results”
  Is XML conversion a panacea? (separate database)
  need appropriate XML form
  sufficiently clear coded concepts
  search by code or search by string, for anatomy, finding, segmented property type, etc.

## Slide 46: Segmentation Object
Just an Enhanced Multi-frame “image”
  Functional Groups and Dimensions
Each frame is (part of) a segment
One slice in space/time
  each pixel (voxel) is either binary (in segment or not) or fractional occupancy/probability
  bits packed into bytes or words
Multiple segments, each numbered
Frames described with “vector” of characteristics
  segment #, position, orientation … order irrelevant

## Slide 47: Segmentation Object
Can overlap
  e.g., one voxel in space may be in multiple segments
  cw. “label map” style encoding with each pixel an index of (one choice) of segment
May be 1:1 with voxels of source image (wasteful)
  or just (3D) bounding box around segmented voxels
  may also be sampled differently, down-sampled or up-sampled in-plane or between slices
May explicitly reference source images
  or be generalized in 3D space (frame of reference UID)
  recipient has to choose which image series

## Slide 48: Enhanced Multi-Frame
More like NRRD (etc.) volume in one “file”
All slices in single DICOM Instance
“Vector” of attributes describing each frame
Attributes grouped with similar siblings
  “functional groups”
Itemized per-frame
  Per-Frame Functional Groups Sequence
  same order as encoded frames in Pixel Data
Commonality factored out
  Shared Functional Groups Sequence

## Slide 49: Multi-frame Functional Groups
Per-frame attributes
Pixel data
Shared attributes

## Slide 50: Enhanced Multi-frame
Single slice
  top level dataset
    Image Position (Patient)
    Image Orientation (Patient)
  Pixel Spacing
Multi-frame
  Shared Functional Group Sequence (1 item)
    Pixel Measures Sequence > Pixel Spacing
    Plane Orientation Sequence > Image Orientation (Patient)
  Per-Frame Functional Group Sequence (n items)
    Plane Position Sequence > Image Position (Patient)

## Slide 51: Enhanced Multi-frame
Single slice
  top level dataset
    Image Position (Patient)
    Image Orientation (Patient)
    Pixel Spacing
Multi-frame
  Shared Functional Group Sequence (1 item)
    Pixel Measures Sequence > Pixel Spacing
    Plane Orientation Sequence > Image Orientation (Patient)
  Per-Frame Functional Group Sequence (n items)
    Plane Position Sequence > Image Position (Patient)
    Frame Content Sequence > Stack ID and In-Stack Position

## Slide 52: Dimensions
Space
5
In-Stack Position
Stack ID = 1
4
3
2
1
Start with a dimension of space.
A set of contiguous slices through the heart.

## Slide 53
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space
Time
5
In-Stack Position
Stack ID = 1
4
3
2
1
5
In-Stack Position
Stack ID = 1
4
3
2
1
Add dimension of time (delay time from R-wave).
Sets of contiguous slices throughout cardiac cycle.

## Slide 54
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (1)
Time (2)
1
\
5
\
2
Dimension Index Values
Dimension Index Pointers:
Stack ID
In-Stack Position
Temporal Position Index
5
In-Stack Position
Stack ID = 1
4
3
2
1
5
In-Stack Position
Stack ID = 1
4
3
2
1

## Slide 55
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (1)
Time (2)
1
\
5
\
2
Dimension Index Values
Dimension Index Pointers:
Stack ID
In-Stack Position
Temporal Position Index
5
1\5\1
In-Stack Position
Stack ID = 1
4
1\4\1
3
1\3\1
2
1\2\1
1
1\1\1
5
1\5\2
In-Stack Position
Stack ID = 1
4
1\4\2
3
1\3\2
2
1\2\2
1
1\1\2

## Slide 56
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (2)
Time (1)
2
\
1
\
5
Dimension Index Values
Dimension Index Pointers:
Temporal Position Index
Stack ID
In-Stack Position
5
1\1\5
In-Stack Position
Stack ID = 1
4
1\1\4
3
1\1\3
2
1\1\2
1
1\1\1
5
2\1\5
In-Stack Position
Stack ID = 1
4
2\1\4
3
2\1\3
2
2\1\2
1
2\1\1

## Slide 57
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (2)
Time (1)
2
\
1
\
5
Dimension Index Values
Dimension Index Pointers:
Trigger Delay Time
Stack ID
In-Stack Position
5
1\1\5
In-Stack Position
Stack ID = 1
4
1\1\4
3
1\1\3
2
1\1\2
1
1\1\1
5
2\1\5
In-Stack Position
Stack ID = 1
4
2\1\4
3
2\1\3
2
2\1\2
1
2\1\1

## Slide 58
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (2)
Time (1)
2
\
5
Dimension Index Values
Dimension Index Pointers:
Trigger Delay Time
Image Position (Patient)
5
1\5
Index of Image Position (Patient)
4
1\4
3
1\3
2
1\2
1
1\1
5
2\5
Index of Image Position (Patient)
4
2\4
3
2\3
2
2\2
1
2\1