## Slide 1: Exploring Peritumoral White Matter Fibers for Neurosurgical Planning
Sonia Pujol, Ph.D.
Ron Kikinis, M.D.
Surgical Planning Laboratory
Harvard University

## Slide 2: Clinical Goal
Diffusion Tensor Imaging (DTI) Tractography has the potential to bring valuable spatial information on tumor infiltration and tract displacement for neurosurgical planning of tumor resection.
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning

## Slide 3: Clinical Case
35 year-old male diagnosed with Glioblastoma multiforme (GBM)
Diffusion Weighted Imaging (DWI) acquisition for neurosurgical planning
White Matter Exploration for Neurosurgical Planning

## Slide 4: Clinical Goal
The goal of this tutorial is
to explore white matter
fibers surrounding a
tumor using Diffusion
Tensor Imaging (DTI)
Tractography.
White Matter Exploration for Neurosurgical Planning
Ventricles
White Matter tracts
Tumor

## Slide 5: Image Analysis Pipeline
The image analysis pipeline
described in this tutorial uses three
different algorithms: the “Grow Cut”
algorithm for segmentation of the
tumor parts, the Marching Cube
algorithm for surface modeling,
and the single tensor
streamline tractography algorithm
for tract generation.
White Matter Exploration for Neurosurgical Planning

## Slide 6: Overview of the analysis pipeline
Part 1: Loading &Visualization of Diffusion Data
Part 2: Segmentation of the ventricles, and solid and cystic parts of the tumor
Part 3: Tractography reconstruction of the white matter fibers in the peri-tumoral volume
Part 4: Tractography exploration of the ipsilateral and contralateral side
White Matter Exploration for Neurosurgical Planning

## Slide 7: Part 1: Loading and Visualization of Diffusion Data
White Matter Exploration for Neurosurgical Planning

## Slide 8: Diffusion Tensor Imaging
zz
zy
zx
yz
yy
yx
xz
xy
xx
D
D
D
D
D
D
D
D
D
D=
(Stejskal and Tanner 1965, Basser 1994 )
White Matter Exploration for Neurosurgical Planning

## Slide 9: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
First, click on Load Data

## Slide 10: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
The “Add data into the scene” window appears. Click Choose Directory to Add

## Slide 11: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Locate and select the file WhiteMatterExplorationData and click Choose

## Slide 12: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Check off the Volumes BaselineVolume.nrrd and DTIVolume.nhdr click OK

## Slide 13: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays the elements of the scene, which contains the MR volume of the brain and a series of 3D surface models

## Slide 14: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Click on the pin icon to display the slice menu, then click on the link icon to link the 3 anatomical viewers. Then change the background so it is set to BaselineVolume

## Slide 15: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the Volumes module from the Modules menu

## Slide 16: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
The user can manually adjust the Window Level editor presets with the Volume module menu

## Slide 17: Loading DTI and Baseline Data
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Click on the Layout menu and select the layout Red slice only

## Slide 18: Part 1: Segmenting the tumor and ventricles
White Matter Exploration for Neurosurgical Planning

## Slide 19: Tumor Segmentation
The tumor in this clinical case is composed of two parts: a solid part, and a cystic part.
In this section, we will segment the different parts of the tumor using a Grow Cut Segmentation algorithm.
Cystic part
Solid part
Tumor
White Matter Exploration for Neurosurgical Planning

## Slide 20: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays only the Axial anatomical slice in the Viewer

## Slide 21: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Click on the Modules menu and select the module Editor

## Slide 22: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
The ‘SlicerApp-real’ window appears. Select the label map GenericAnatomyColors and click Apply

## Slide 23: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the PaintEffect tool

## Slide 24: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Scroll down the Editor module and choose color #293 for the region 1 label

## Slide 25: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
In a single motion, draw a short line in the cystic part of the tumor

## Slide 26: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select color #7 for the mass label and, again in a single motion, draw a short line in the solid part of the tumor

## Slide 27: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select color #295 for region 3 and draw a circle around the tumor

## Slide 28: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the GrowCutEffect tool

## Slide 29: Grow Cut Segmentation
The Grow Cut Segmentation method is a competitive region growing algorithm using Cellular Automata.
The algorithm performs multi-label image segmentation using a set of user input scribbles.
V. Vezhnevets, V. Konouchine. "Grow-Cut" - Interactive Multi-Label N-D Image Segmentation". Proc. Graphicon. 2005 . pp. 150–156.
White Matter Exploration for Neurosurgical Planning
Notes: The pixel labelling process can be seen as
growth and struggle for domination of K types of bacteria. The bacteria
start to spread (grow) from the seed pixels and try to occupy
all the image.

## Slide 30: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Click Apply to apply the GrowCutEffect segmentation algorithm

## Slide 31: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays the results from the segmentation
Solid part
Cystic part

## Slide 32: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Scroll up the Editor menu and select the tab Per-Structure Volumes. Then click Split Merge Volume

## Slide 33: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
The label map BaselineVolume-label has been split into three volumes:
BaselineVolume-mass-label: solid part of the tumor
BaselineVolume-region_1-label: cystic part of the tumor
BaselineVolume-region_3-label: surrounding structures

## Slide 34: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Click on the Modules menu and select the Module Data

## Slide 35: Tumor Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
The different label maps have been generated

## Slide 36: Ventricles Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Go back to the Editor module

## Slide 37: Ventricles Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the volume
BaselineVolume-region_3-label so that it is highlighted and that the yellow region is visible in the viewer

## Slide 38: Ventricles Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the ThresholdEffect tool

## Slide 39: Ventricles Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Scroll down the Editor module and set the lower Threshold Range to 1700 and click Apply

## Slide 40: Ventricles Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays the result of the threshold

## Slide 41: Ventricles Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the SaveIslandEffect in the Editor module

## Slide 42: Ventricles Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
With the SaveIslandEffect tool equipped, click in the occipital horn of the ventricle

## Slide 43: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays the result of the segmentation of the ventricles.

## Slide 44: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Scroll back up and click on Merge and Build to merge the different label maps, and generate the 3D models of the tumor and ventricles using a Marching Cubes algorithm

## Slide 45: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays the results of the merging of the segmentations of the ventricles and the tumor in the Viewer

## Slide 46: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Click on the Layout menu and select Conventional

## Slide 47: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays the 3D surface reconstructions of the ventricles, and solid and cystic parts of the tumor.

## Slide 48: Definition of peri-tumoral volume
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Position the mouse over the pin icon, deselect the link icon, and select the eye icon to view just the axial slice in the 3D Viewer

## Slide 49: Definition of peri-tumoral volume
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the label map BaselineVolume-region_1-label (blue) and select the DilateEffect tool

## Slide 50: Part 2: Tractography exploration of peri-tumoral white matter fibers
White Matter Exploration for Neurosurgical Planning

## Slide 51: Definition of peri-tumoral volume
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
With the DilateEffect tool equipped, click on the cystic part of the tumor in the axial slice viewer once, then select Apply 3 times to generate the peritumoral volume

## Slide 52: Definition of DTI volume
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Note the dilatation of the cystic part of the tumor in the 3D viewer

## Slide 53: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the module Tractography Label Map Seeding

## Slide 54: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
- I/O: Set the following input and output volume:
Input DTI Volume: DTIVolume
Input Label Map: BaselineVolume-region_1-label
Output Fiber Bundle: Create and rename newFiberBundle

## Slide 55: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Scroll down and set the following values:
- Seed Placement Options:
Check Use Index Space
Stopping Value
Set the FA threshold to 0.15
- Label Definition:
Enter Seeding Label 293, and Click on Apply

## Slide 56: Final Result of Segmentation
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Slicer displays the white matter fibers surrounding the tumor
The fibers are colored according the fractional anisotropy values
(red = low ; blue,green = high)

## Slide 57: Part 4: Tractography exploration of the ipsilateral and contralateral side
White Matter Exploration for Neurosurgical Planning

## Slide 58: Tractography on-the-fly
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Click on the Modules menu and select the module Tractography Interactive Seeding

## Slide 59: Tractography on-the-fly
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Position the mouse over the pin icon in the axial slice viewer and change the volume to DTIVolume

## Slide 60: Tractography on-the-fly
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Select the Fiducial icon, and position it next to the cystic part of the tumor by clicking near it in the 3D viewer

## Slide 61: Tractography on-the-fly
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Set Input DTI Volume to DTIVolume
Set Fiducial List or Model to F
Set Output Fiber Bundle to Create new Fiber Bundle

## Slide 62: Tractography on-the-fly
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Scroll down the module and set the Minimum Path Length to 10.0 mm and the FA Stopping Value at 0.15

## Slide 63: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Position the fiducial in the cingulum on the contralateral side opposite to the tumor

## Slide 64: Tractography on-the-fly
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
White Matter Exploration for Neurosurgical Planning
Explore the aspect of the cingulum in the contralateral and ipsilateral sides

## Slide 65: Conclusion
Fully integrated pipeline for semi-automated tumor segmentation and white matter tract reconstruction
3D interactive exploration of the white matter tracts surrounding a tumor (peri-tumoral tracts) for neurosurgical planning
White Matter Exploration for Neurosurgical Planning

## Slide 66: Acknowledgments
White Matter Exploration for Neurosurgical Planning
National Alliance for Medical Image Computing (NA-MIC)
NIH U54EB005149
Neuroimage Analysis Center (NAC)
NIH P41RR013218
Parth Amin, WIT ’16
Matthew Flynn, WIT ‘16