## Slide 1: 3D Slicer hands-on tutorial
Csaba Pinter Kingston, ON, Canada
http://perk.cs.queensu.ca

## Slide 2: Platform and hardware
Developed and maintained on Windows 64bit, Mac OSX, and Linux 64bit & 32bit
Slicer requires
  Minimum 2GB RAM
  Graphics accelerator with 64MB of memory
  64 bit strongly suggested

## Slide 3: 3D Slicer version 4.5
The Welcome module appears at start-up

## Slide 4: Welcome to Slicer
Each module includes a series of sections, which give access to different functionalities.
Click on the arrow to open

## Slide 5: Welcome to Slicer
The Main Window section contains information on the basic organization of Slicer’s user interface

## Slide 6: Slicer user interface
Main menu
Toolbar
3D viewer
2D anatomical viewers
Data probe
Module panel

## Slide 7: Welcome module
The Documentation & Tutorial section contains links to the Slicer training compendium and documentation

## Slide 8: Welcome module
The Welcome module panel contains shortcuts for loading different types of data. A series of sample data are also available.
Click on Download Sample Data to access the Sample Data Module

## Slide 9: Sample Data
The Sample Data module contains links to 12 different sample datasets that can be downloaded into Slicer

## Slide 10: Sample Data
Brain MRI
Chest CT
Cardiac CT
Diffusion Tensor Imaging
Brain MRI (tumor patient)
Image is courtesy of Sonia Pujol, PhD

## Slide 11: Sample Data
Click on Download MRHead to download the dataset in Slicer

## Slide 12: Sample Data
The brain MR image appears in the 2D viewers

## Slide 13: MR Brain Sample Dataset
Position the mouse on the little pin icon in the top left corner of a 2D viewer to display the viewer menu

## Slide 14: MR Brain Sample Dataset
Click on the link icon to link 2D viewers, then on the eye icon to display slices in the 3D viewer

## Slide 15: MR Brain Sample Dataset
The axial, coronal, and sagittal slices appear in the 3D view. Go back to the Welcome module using the green arrow in the toolbar

## Slide 16: MR Brain Sample Dataset
Click on the Mouse & Keyboard section to learn the different mouse actions to rotate and zoom

## Slide 17: Load data from file
Data can be loaded from files using the Add data dialog, or by drag&dropping files onto the Slicer window

## Slide 18: Load DICOM data
DICOM data can be loaded using the DICOM browser after importing it to the DICOM database

## Slide 19: Changing layout
Choose Red slice only

## Slide 20: Slice viewer toolbar cont’d
Hover the pin again, and once the slice viewer toolbar is displayed, click on “>>”

## Slide 21: Slice viewer toolbar cont’d
This menu will appear once the “>>” button is pressed

## Slide 22: Lightbox view
Click on the Lightbox menu choose the “3x3 view”

## Slide 23: Lightbox view
9 consecutive images of the DICOM volume are displayed. Use the red slice slider (or the mouse wheel) to browse through the data

## Slide 24: Switch back the layout
Choose Four-up

## Slide 25: Turn off lightbox view
Choose 1x1 view

## Slide 26: Close Slicer scene

## Slide 27: Download Slicer scene
Download file http://www.slicer.org/slicerWiki/images/c/c4/Slicer4minute.zip
A Slicer scene is a MRML (Medical Reality Modeling Language) file containing a list of elements loaded into Slicer (volumes, etc.)
The scene file and datasets have been saved as an MRB (Medical Reality Bundle) file
MRB is Slicer’s archive file format

## Slide 28: Load scene
Load slicer4minute.mrb into Slicer using the Add data dialog or drag&drop

## Slide 29: Subject hierarchy
Switch to the Subject hierarchy module and choose “Yes to All”

## Slide 30: Subject hierarchy
Show/hide objects by clicking the eye icon

## Slide 31: Subject hierarchy
Organize data into hierarchies: Create subject after right-clicking the Scene

## Slide 32: Subject hierarchy
Rename objects by double clicking their names

## Slide 33: Subject hierarchy
Select multiple items by holding down shift
Move objects by drag&drop

## Slide 34: Subject hierarchy
Find object-specific actions in the context menus by right-clicking the different items. Right-click skull_bone and select “Edit properties...”

## Slide 35: Subject hierarchy
Edit properties switched to the Models module and selected the object. Models module also can be reached from the toolbar or the module list

## Slide 36: 3D visualization
Turn on slice display for only the red slice

## Slide 37: 3D visualization
Use the slider or the mouse wheel to browse through the axial MR slices

## Slide 38: 3D visualization
Show skin again by clicking the eye icon
Open the display tab
Use Opacity slider to make the skin semi-transparent

## Slide 39: 3D visualization
Hide skin and skull bone
Turn on coronal slice visibility

## Slide 40: 3D visualization
Select hemispheric_white_matter
Turn on Clip in the Display options

## Slide 41: 3D visualization
In the Clipping section, select Green Slice Clipping: Negative.
Scroll coronal slice to reveal the optic chiasm

## Slide 42: 3D visualization
Turn off clipping
Turn on Slicer Intersections Visible
Hide coronal slice from 3D view

## Slide 43: 3D visualization
Switch to Four-Up layout
Show skin
Move the mouse over the pin in the corner of the 3D view
Select A (Anterior) view
Notes: You can reset the view by clicking the little button to the left of the slice view sliders

## Slide 44: Saving a scene
Click on Save button

## Slide 45: Saving a scene
Rename scene

## Slide 46
Thank you for your attention!

## Slide 48
Appendix