## Slide 2
--
CTSA at RSNA 2010
An end-user application for image analysis and visualization
An open-source environment for software development
A software platform that is both easy to use for clinical researchers and easy to extend for programmers

## Slide 3
--
CTSA at RSNA 2010
Disclaimer
It is the responsibility of the user of 3DSlicer to comply with both the terms of the license and with the applicable laws, regulations and rules. Slicer is a tool for research, and is not FDA approved.
3D Slicer version 3 is a multi-platform software running on Windows, Linux, and Mac OSX.
www.slicer.org

## Slide 4
--
CTSA at RSNA 2010
This workshop uses the newest release of 3D Slicer (version 3.6.2).
Visit the Slicer download page for Slicer 3.6 stable release, or for Slicer nightly builds.

## Slide 5
--
CTSA at RSNA 2010
Getting Started: Slicer3 Minute Tutorial
Quantitative Measurement of Volumetric Change: ChangeTracker Tutorial
Quantitative Measurements for Functional Imaging: PETCTFusion Tutorial
All Tutorial Datasets are located in C:\slicer_data
Tutorial Overview

## Slide 6
--
CTSA at RSNA 2010
Tuning up…
Setting Font Size
In Slicer’s main menu, select
View->Application Settings

## Slide 7
--
CTSA at RSNA 2010
Tuning up…
Setting Font Size
This raises Slicer’s Application Settings Interface
In the left panel, select
Font Settings

## Slide 8
--
CTSA at RSNA 2010
Tuning up…
Setting Font Size
This displays Slicer’s Font Family and Font Size options
Choose among options until you find a font-size that works well for you.
Slicer will remember these settings next time you start the application.

## Slide 9
--
CTSA at RSNA 2010
This tutorial is a short introduction to the advanced 3D visualization capabilities of the Slicer3 software for medical image analysis.
It is designed to quickly build a basic level of comfort with the Slicer software.
Slicer3 Minute Tutorial
Part I: Slicer3 Minute Tutorial
Sonia Pujol, PhD
Wendy Plesniak, PhD

## Slide 10
--
CTSA at RSNA 2010
http://www.spl.harvard.edu/publications/item/view/1265
Slicer3 Minute Tutorial
The Slicer3Minute dataset is composed of
An MR scan of the brain and 3D surface
Reconstructions of anatomical structures.
The data are part of the SPL-PNL Brain Atlas
Developed by Talos et al. The atlas is available at:

## Slide 11
--
CTSA at RSNA 2010
Windows users:
Double-Click the Shortcut to Slicer3.exe on the Desktop
or Select
Slicer3 Minute Tutorial: Launch the Application
Start ->All Programs ->Slicer3 3.5.2009-11-06->Slicer

## Slide 12
--
CTSA at RSNA 2010
The Graphical User Interface (GUI) of Slicer3 integrates five components:
the Menu Toolbar
the Module GUI Panel
the 3D Viewer
the Slice Viewer
the Slice and 3D View Controller
Slice Viewers
3D Viewer
Module GUI Panel
Slice and 3D View Controller
Menu & Toolbar
Slicer3 Minute Tutorial: Navigating the Application GUI

## Slide 13
--
CTSA at RSNA 2010
The SlicerWelcome module is the module displayed by default.
This module gives an overview of the GUI of Slicer3, and data loading & saving functionalities.
Slicer3 Minute Tutorial: Welcome Module

## Slide 14
--
CTSA at RSNA 2010
Expand or shrink the GUI panel with the arrows at the frame top, or by clicking and dragging the vertical separator
Expand or collapse any sub-panel by clicking on its grey title bar.
Slicer3 Minute Tutorial: GUI Basics

## Slide 15
--
CTSA at RSNA 2010
Browse to the location of the Slicer_data directory.
Select that directory and select the Add To Favorites
icon
This will make the directory easier to find later...
Select File-> Load Scene from the File menu
Slicer3 Minute Tutorial: Load A Scene

## Slide 16
--
CTSA at RSNA 2010
Browse to the location of the Slicer3MinuteDataset directory.
Select the scene file slicer3minute.mrml
Click on Open to load the scene
Slicer3 Minute Tutorial: Load A Scene

## Slide 17
--
CTSA at RSNA 2010
When the scene is finished loading, Slicer displays:
a 3D model of the head in the 3D Viewer, and
anatomical MR slices of the brain in the 2D Slice Viewers.
3D Viewer
2D Slice Viewers
Slicer3 Minute Tutorial: Viewing the Scene

## Slide 18
--
CTSA at RSNA 2010
Note:
We have pre-adjusted the window and level settings for these volumes so that they are appropriate for display on most laptops.
If display is not satisfactory on your machine or projector, the Volumes Module may be used to refine these settings.
Slicer3 Minute Tutorial: Viewing the Scene

## Slide 19
--
CTSA at RSNA 2010
Left click and hold the Modules menubutton.
Select All Modules to display the many modules available for image processing, analysis and 3D visualization.
Slicer3 Minute Tutorial: Exploring Slicer’s functionality

## Slide 20
--
CTSA at RSNA 2010
To access the Models module, browse through the list of modules...
...or click on the models icon in the toolbar
Slicer3 Minute Tutorial: Exploring Slicer’s functionality

## Slide 21
--
CTSA at RSNA 2010
Slicer displays the GUI of the Models module.
Slicer3 Minute Tutorial: Switching to the Models Module

## Slide 22
--
CTSA at RSNA 2010
Position the mouse in the 3D Viewer.
Hold down the left mouse button and drag to rotate the model.
Slicer3 Minute Tutorial: Basic 3D Interaction
Left-click & drag

## Slide 23
--
CTSA at RSNA 2010
Click on the Slice Visibility icon
to display the Axial Slice in the 3D Viewer
Slicer3 Minute Tutorial: Viewing Slices in the 3D Viewer

## Slide 24
--
CTSA at RSNA 2010
Slicer adds a view of the Axial slice in the 3D View.
Slicer3 Minute Tutorial: 3D Visualization

## Slide 25
--
CTSA at RSNA 2010
Select the Skin model.
Change the opacity of the model from 1.0 to 0.0.
Slicer3 Minute Tutorial: 3D Visualization

## Slide 26
--
CTSA at RSNA 2010
The model of the skull bone and eyeballs become visible through the model of the skin in the 3D viewer.
(skin model opacity = 0.5)
Slicer3 Minute Tutorial: 3D Visualization

## Slide 27
--
CTSA at RSNA 2010
The model of the skin becomes invisible in the 3D viewer.
(skin model opacity = 0.0)
(skull model opacity = 1.0)
Slicer3 Minute Tutorial: 3D Visualization

## Slide 28
--
CTSA at RSNA 2010
Slicer3 Minute Tutorial: 3D Visualization
Click on the Slice Visibility icon in the Green Slice Viewer
to display the Coronal Slice in the 3D Viewer.

## Slide 29
--
CTSA at RSNA 2010
Slicer3 Minute Tutorial: 3D Visualization
Select the 3D model skull_bone.vtk in the Model Hierarchy and turn on the Clipping option.

## Slide 30
--
CTSA at RSNA 2010
Slicer3 Minute Tutorial: 3D Visualization
Browse through the coronal slices to expose the 3D model of the white matter, and the left and right optic nerves.

## Slide 31
--
CTSA at RSNA 2010
Select the 3D model “skull_bone” in the Model Hierarchy, and turn off its Visibility
Slicer3 Minute Tutorial: 3D Visualization

## Slide 32
--
CTSA at RSNA 2010
Scroll the Coronal Slices to display the hemispheric white matter model in the context of the image data in the 3D Viewer.
Slicer3 Minute Tutorial: 3D Visualization

## Slide 33
--
CTSA at RSNA 2010
Select the hemispheric white matter model called
hemispheric_white_matter.vtk
Turn off its visibility.
Slicer3 Minute Tutorial: 3D Visualization

## Slide 34
--
CTSA at RSNA 2010
Slicer displays the optic nerve, optic chiasm and optic tracts overlaid on the MR images of the brain.
Slicer3 Minute Tutorial: 3D Visualization

## Slide 35
--
CTSA at RSNA 2010
Windows/Linux users: Position the mouse in the 3D Viewer, hold down the right mouse button and move the mouse down to zoom in.
Mac users: Position the mouse in the 3D Viewer, hold down the apple button and the mouse button and move the mouse down to zoom in.
Slicer3 Minute Tutorial: 3D Visualization: Zoom the view

## Slide 36
--
CTSA at RSNA 2010
Slicer3 displays a closer view of 3D anatomical structures overlaid on 2D MR slices
Slicer3 Minute Tutorial: 3D Visualization

## Slide 37
--
CTSA at RSNA 2010
This tutorial has demonstrated:
Basic description of the Slicer3 Application Interface
How to load a scene containing volumes and models
How to visualize these different datasets together
Next, we will use these building blocks to perform image analysis and visualize quantitative results.
Slicer3 Minute Tutorial: Summary

## Slide 38
--
CTSA at RSNA 2010
The module described in this tutorial was tested on Axial 3D SPGR T1 post Gadolinium scans (Voxel dimension: 0.94mm x 0.94mm x 1.20mm, FOV: 240mm, Matrix: 256 x 256)
Part II: Analyzing Small Volumetric Changes using the ChangeTracker Module
Kilian M Pohl, PhD
Ender Konugolu, PhD
Andriy Fedorov, PhD
ChangeTracker: exploring small volumetric changes

## Slide 39
--
CTSA at RSNA 2010
Conventional anatomic imaging using CT or MRI are often used to evaluate tumor size and shape
Most clinical trials that evaluate new chemotherapeutic drugs use changes in uni-dimensional or bi-dimensional measurements to assess response (e.g. RECIST)
Slicer has several tools for applying RECIST methodologies
ChangeTracker: Conventional measures of tumor response

## Slide 40
--
CTSA at RSNA 2010
The distance measurement (mm) between fiducials will be updated in the Fiducial’s GUI.
3D Slicer’s Fiducials Module can be used to measure the longest diameter
in a tumor cross section.
Two fiducials may be used to mark the tumor’s extent.
Quantifying tumor change: Conventional measures of tumor response

## Slide 41
--
CTSA at RSNA 2010
3D Slicer’s Measurements module, provides interactive measurement tools that operate in the 3D Viewer and the Slice Viewers.
Interactive ruler can be used to measure the longest diameter and provides numerical annotations
Quantifying tumor change: Conventional measures of tumor response

## Slide 42
--
CTSA at RSNA 2010
3D Slicer’s LabelDiameterEstimation (extension) module will automatically compute the largest tumor diameter and orthogonal dimension.
This analysis requires an initial segmentation (VOI).
Baseline: June 2006 Follow-up: June 2007
Quantifying tumor change: Conventional measures of tumor response

## Slide 43
--
CTSA at RSNA 2010
However, more accurate and precise methods for understanding volume changes may be useful when:
benign tumor change is being monitored, or
where small changes may be clinically significant but difficult to assess with RECIST
ChangeTracker: rationale for new approaches
ChangeTracker Module is a tool to measure volumetric change at the voxel level.

## Slide 44
--
CTSA at RSNA 2010
First, close any previous scene.
Select File->Close Scene
This removes any datasets previously loaded into Slicer.
ChangeTracker: exploring small volumetric changes

## Slide 45
--
CTSA at RSNA 2010
Select File->Load Scene
This raises the Load Scene Interface
Select Slicer_data from favorites panel.
Select the ChangeTracker2010 directory
And select the scene file: ChangetrackerTutorial2009.mrml
double click the file, or click Open
ChangeTracker: Load the training dataset

## Slide 46
--
CTSA at RSNA 2010
This course is built upon two scans of a patient with meningioma:
MR Scan 1
MR Scan 2
Please note: we have pre-adjusted the window and level settings for these volumes so that they are appropriate for display on most laptops. If display is not satisfactory on your machine or projector, the Volumes Module may be used to refine these settings.
ChangeTracker: about the data...

## Slide 47
--
CTSA at RSNA 2010
Meningoma
Usually benign slow-growing tumors
Baseline radiologist’s clinical impression:
large falcine lesion is identified.
measures 3.1 cm anteroposteriorly, 3.05 cm from side-to-side, 3.5 cm in height.
enhances moderately on post gadolinium imaging.
Follow-up radiologist’s clinical impression:
left frontal lobe mass appears unchanged on all series.
measures 3.3 x 3.2 cm in maximum dimension.
enhances moderately on post gadolinium imaging.
How has the tumor changed?
Baseline: June 2006
Follow-up: June 2007
ChangeTracker: Clinical context

## Slide 48
--
CTSA at RSNA 2010
Change Layout to “Four-up”:
Using the Layout Menubutton,
Select Four-up layout.
ChangeTracker: exploring small volumetric changes

## Slide 49
--
CTSA at RSNA 2010
Using the Modules Menubutton,
Select the ChangeTracker Module from the Wizards category.
ChangeTracker: exploring small volumetric changes

## Slide 50
--
CTSA at RSNA 2010
A Workflow Wizard guides the user through a sequence of steps and has the following components:
the Step Panel
the User Panel
the Navigation Panel
ChangeTracker: a note about the Workflow Wizard
Step Panel--
User Panel--
Navigation Panel--

## Slide 51
--
CTSA at RSNA 2010
Select baseline & follow-up studies:
Scan 1 = 2006-spgr
Scan 2 = 2007-spgr
ChangeTracker: First step: select scans

## Slide 52
--
CTSA at RSNA 2010
Move sliders in Slice Viewer Control panels to get a close-up view of tumor in Axial, Sagittal and Coronal slice viewers.
Zoom in (Right mouse down and push/pull).
Pan (Middle mouse down and move).
Press Next
ChangeTracker: inspect the tumor

## Slide 53
--
CTSA at RSNA 2010
A VOI Box Widget is positioned within the image volume in the 3D viewer, and the VOI’s intersection with each slice is shown in blue.
Center the VOI first:
Right mouse click in the tumor center to position the VOI displayed in blue in each Slice Viewer.
ChangeTracker: Step 2. Define a volume of interest

## Slide 54
--
CTSA at RSNA 2010
View the VOI box widget and volume rendering of tumor in yellow in the 3D Viewer
Next, resize the VOI:
Left mouse click in any Slice Viewer to change the VOI extent
ChangeTracker: Step 2. Define a volume of interest

## Slide 55
--
CTSA at RSNA 2010
Note: VOI Widget range sliders are color-coded to match VOI box Widget handles in 3D Viewer
Fine-tune the VOI using the VOI Widget range sliders or by moving the VOI Widget handles in 3D view
ChangeTracker: Step 2. Define a volume of interest

## Slide 56
--
CTSA at RSNA 2010
Scroll through slices to ensure that tumor boundaries are included in the VOI.
Click Next
ChangeTracker: Step 2. Define a volume of interest

## Slide 57
--
CTSA at RSNA 2010
ChangeTracker: Step 3. Segment the tumor
Make sure that the volume called 2006_spgr.nrrd_VOI_Supersampled is selected in the background layer
...and...2006_spgr.nrrd_VOI_PresSegmented is selected in the label layer.

## Slide 58
--
CTSA at RSNA 2010
Slice Viewers show VOI with current segmentation overlay in light yellow
3D Viewer shows model of tumor
Modify the segmentation by moving threshold range slider
ChangeTracker: Step 3. Segment the tumor

## Slide 59
--
CTSA at RSNA 2010
Scroll through the slices until the segmentation appears optimal.
ChangeTracker: Step 3. Segment the tumor
Press Next.

## Slide 60
--
CTSA at RSNA 2010
ChangeTracker: Step 3. Segment the tumor
Press the Slice option to view the volume rendered segmentation with the axial slice together.
If you need to reset the 3D View, try using the Axis Navigator Widget.

## Slide 61
--
CTSA at RSNA 2010
Metric Options:
Detect change by analyzing intensity pattern (fast)
Measure change by analyzing deformation map (slow)
Select fast and press Analyze
ChangeTracker: Final step: Select Metric

## Slide 62
--
CTSA at RSNA 2010

## Slide 63
--
CTSA at RSNA 2010
Change in volume is shown overlaying the tumor image and in the 3D Viewer: magenta = growth green = shrinkage
ChangeTracker: Results: change in pathology
Note: Analysis is displayed in the “Compare View” layout with linked control for the compare Viewers.

## Slide 64
--
CTSA at RSNA 2010
ChangeTracker: Results: change in pathology
Select visibility icon to show axial slice in the 3D Viewer.

## Slide 65
--
CTSA at RSNA 2010
“Compare View” layout displays:
Axial slice & 3D View
Five corresponding consecutive slices for the VOI in the baseline (top row), and
in the followup (bottom row).
ChangeTracker: Results: change in pathology

## Slide 66
--
CTSA at RSNA 2010
Crosshairs in Compare View show corresponding voxels in baseline and followup scan for voxel-wise comparison.
ChangeTracker: Results: change in pathology

## Slide 67
--
CTSA at RSNA 2010
Modify sensitivity of intensity pattern analysis
sensitive
moderate
robust
ChangeTracker: Exploring small volumetric changes

## Slide 68
--
CTSA at RSNA 2010
Click on the colored bar at the top of any Slice Viewer to show or hide the controls.
This allows more display space for viewing the image data.
ChangeTracker: Exploring small volumetric changes

## Slide 69
--
CTSA at RSNA 2010
Tested on Axial 3D SPGR T1 post Gadolinium scans (Voxel dimension: 0.94mm x 0.94mm x 1.20mm, FOV: 240mm, Matrix: 256 x 256).
Tumor boundary should be clear.
Only for contrast enhanced images.
Need homogenous enhancement across timepoints.
Not tested for tumors with changing necrosis.
Correspondence between Intensity-based and deformation mapping-based analyses should be checked.
ChangeTracker: Exploring small volumetric changes

## Slide 70
--
CTSA at RSNA 2010
This tutorial demonstrated:
a method to quantify small volumetric changes in pathology.
visualization of these changes in the anatomical context
use of Slicer’s “Compare Viewer” to simultaneously explore baseline and followup studies.
Next, we will demonstrate combined visualization of PET/CT studies and SUV computation.
ChangeTracker: exploring small volumetric changes

## Slide 71
--
CTSA at RSNA 2010
Part III: PET/CT Analysis using 3D Slicer
Jeffrey Yap PhD
Ron Kikinis MD
Wendy Plesniak PhD
PET/CT Visualization and Analysis

## Slide 72
--
CTSA at RSNA 2010
PET/CT Visualization and Analysis: Start fresh.
First, close any previous scene.
Select File->Close Scene
This removes any datasets previously loaded into Slicer.

## Slide 73
Select File->Load Scene
--
CTSA at RSNA 2010
This raises the Load Scene Interface
select the file called
PETCTFusion-Tutorial-Scene.mrml
Double click the file, or click Open
PET/CT Visualization and Analysis: Load the new scene

## Slide 74
--
CTSA at RSNA 2010
Non small cell lung cancer patient
Two PET studies: baseline acquired before treatement, and followup acquired 1 month after chemotherapy
Two non-diagnostic CT images are acquired without the use of contrast
FDG-PET scans acquired 60 minutes after intravenous injection of approximately 20 mCi of 18FDG
Two VOIs have been created using Slicer’s Editor Module.
PET/CT Visualization and Analysis: About the data

## Slide 75
--
CTSA at RSNA 2010

## Slide 76
--
CTSA at RSNA 2010
In the Data Fusion panel, select:
CT volume: CT1
PET volume: PET1
Tumor Mask: PET1-label
When the PET volume is selected, a “wait message” will be displayed while parameters are read from DICOM header.
Note: Module requires DICOM format data
PET/CT Visualization and Analysis: Select baseline study

## Slide 77
--
CTSA at RSNA 2010
Note: this stacks the PET, CT and VOI in three layers:
Background = CT1
Foreground = PET1
Overlay (Label) = PET1-label
where they can be blended into a single visualization
PET/CT Visualization and Analysis: Information displayed in “Layers”

## Slide 78
--
CTSA at RSNA 2010
In the Display Panel, choose a colorization option for the PET volume from among
Grey, Heat, or Spectrum.
Adjust the window and level for CT1 and PET1 volumes.
Adjust the Slices Fade Scale to jointly display the datasets in the foreground and background layers.
PET/CT Visualization and Analysis: Adjust display of the baseline study

## Slide 79
--
CTSA at RSNA 2010
Explore:
in the Slice Viewers, scroll through the slices to locate the green Tumor label and the yellow Liver label.
Note: (the yellow label is used only to demonstrate multiple-VOI functionality).
PET/CT Visualization and Analysis: Explore the visualization

## Slide 80
--
CTSA at RSNA 2010
Shortcut: To view the Tumor Label in all Slice Viewers:
Enter –740 in the Axial Slice Viewer’s Slice Number Entry
…and…
-54 (Sagittal)
103 (Coronal).
These are (mm) positions within the reference frame of the image volumes.
PET/CT Visualization and Analysis: View tumor in all slice viewers

## Slide 81
--
CTSA at RSNA 2010
SUVmax and SUVmean for each VOI (represented by a different color in the label map) will be displayed in the table.
In the Quantitative Measures panel, click the Compute/Refresh button.
PET/CT Visualization and Analysis: Compute SUV for all VOIs in baseline

## Slide 82
--
CTSA at RSNA 2010
Look for response to treatment in the follow-up study:
In the Data Fusion panel, set:
CT volume = CT2,
PET volume = PET2 and Tumor Mask = PET2-label.
This dataset contains two VOIs that correspond to the segmentations the baseline study.
PET/CT Visualization and Analysis: Compute SUVbw for follow-up study

## Slide 83
--
CTSA at RSNA 2010
Adjust the display for the follow-up study.
You may want to adjust the Slices Fade Slider and manipulate the 3D View to refresh them.
PET/CT Visualization and Analysis: Modify display of the follow-up

## Slide 84
--
CTSA at RSNA 2010
In the “Quantitative Measures” Panel:
select Compute/Refresh to compute SUVbw for the green Tumor volume (and yellow liver volume).
PET/CT Visualization and Analysis: Compute SUVbw for follow-up

## Slide 85
--
CTSA at RSNA 2010
Pre-Treatment Max SUVbw =
Post-Treatment Max SUVbw =
8.0
9.4
+16.61% (SD)
PET/CT Visualization and Analysis: Assess response wrt this VOI

## Slide 86
--
CTSA at RSNA 2010
Still validating this module against performance of commercial systems.
Appropriate only for DICOM PET studies only
Not compatible with Philips datasets
PET/CT Visualization and Analysis: Appropriate Use

## Slide 87
--
CTSA at RSNA 2010
This workshop has demonstrated:
Basic scene loading and visualization using 3D Slicer
Use of Slicer’s ChangeTracker module to assess small changes in tumor size
Workflow to make quantitative measurements of SUV (body weight) in Slicer’s PETCTFusion module
Workshop Summary

## Slide 88
--
CTSA at RSNA 2010
Tutorial Slides:
http://wiki.na-mic.org/Wiki/images/4/4e/Combined-RSNA09-WJP.ppt
Tutorial Data:
http://wiki.na-mic.org/Wiki/images/5/51/Slicer3MinuteDataset.zip
http://wiki.na-mic.org/Wiki/images/f/f8/RSNA-ChangeTracker-Tutorial-Data.zip
http://wiki.na-mic.org/Wiki/images/7/73/PETCTFusion-Tutorial-Data.zip
Tutorial Software:
http://www.na-mic.org/Slicer/Download/Snapshots/win32/Slicer3-3.5-RSNA-2009-11-06-win32.exe
More Information:
http://www.slicer.org
Workshop Summary: Slides and Datasets

## Slide 89
--
CTSA at RSNA 2010
Harvard Clinical and Translational Science Center
National Alliance for Medical Image Computing NIH U54EB005149
Brain Science Foundation
INRIA, France
Neuroimage Analysis Center (NAC)
National Center for Image-Guided Therapy (NCIGT)
Surgical Planning Laboratory, Brigham and Women’s Hospital
Acknowledgements