## Slide 1: 3D VISUALIZATION OF DICOM IMAGES FOR RADIOLOGICAL APPLICATIONS
Sonia Pujol, PhD
Brigham and Women’s Hospital, Harvard Medical School
Kitt Shaffer, MD, PhD
Boston University School of Medicine
Ron Kikinis, MD,
Brigham and Women’s Hospital, Harvard Medical School

## Slide 2: 3D Visualization of DICOM images for Radiological applications
Following this tutorial, you will be able to load and visualize DICOM volumes with 3D Slicer, and to interact in 3D with structural images and models of the anatomy.

## Slide 3: Overview
Part I: Introduction to the 3DSlicer software
Part II: 3D Data Loading and visualization of DICOM images
- Volume Rendering of thoraco-abdominal CT data
- Surface Rendering of MR head data
Part III: 3D interactive exploration of the anatomy
- Exploration of the Segments of the liver
- Exploration of the Segments of the lung

## Slide 4: Overview
Part I: Introduction to the 3DSlicer software
Part II: 3D Data Loading and visualization of DICOM images
- Volume Rendering of thoraco-abdominal CT data
- Surface Rendering of MR head data
Part III: 3D interactive exploration of the anatomy
- Exploration of the Segments of the liver
- Exploration of the Segments of the lung

## Slide 5
Introduction to the 3DSlicer software

## Slide 6: 3DSlicer
3DSlicer is a freely available open-source platform for segmentation, registration and 3D visualization of medical imaging data.
3DSlicer is a multi-institutional effort supported by the National Institute of Health.

## Slide 7: 3DSlicer History
Image Courtesy of the CSAIL, MIT
1997: Slicer started as a research project between the Surgical Planning Lab (Harvard) and the CSAIL (MIT)

## Slide 8: 3DSlicer History
1997: Slicer started as a research project between the Surgical Planning Lab (Harvard) and the CSAIL (MIT)
2013: Multi-institution effort to share the latest advances in image analysis with the clinical and scientific community

## Slide 9: A multi-institution effort
PI: Ron Kikinis, M.D.
PIs: Ferenc Jolesz, M.D., Clare Tempany, M.D.

## Slide 10: An interdisciplinary platform
An end-user application for
clinical investigators and scientists
An open-source environment for software developers
A software platform that is both easy to use for clinical researchers and easy to extend for programmers

## Slide 11: Slicer: Behind the scenes
Slicer is built every night on Windows, Mac and Linux platforms

## Slide 12: Slicer Training events
Hands-on training workshops at national and international venues
More than 2,700 clinicians, clinical researchers and scientists trained since 2005

## Slide 13: Slicer Training events
RSNA 2011
Major international conferences
  RSNA 2008, 2009, 2010, 2011, 2012,2013
  MICCAI 2008, 2009, 2011, 2012,2013
  SfN 2009, 2011
  SPIE 2012, 2013
  CAOS 2010
  CARS 2010, 2012, 2013

## Slide 14: An extensible platform
3D Slicer supports plug-ins called Slicer extensions available from the Extension Manager
Allows end-users to select extensions useful to them, without having to download the entire extension archive.
Built Nightly with Slicer

## Slide 15: Slicer clinical applications
Driving Biological Projects leading to the development of new tools
Applied science oriented toward subject specific analysis in the presence of pathology

## Slide 16: Examples of clinical applications
Radiotherapy: RT-specific analysis dose accumulation and dose comparison (G.Fichtinger et al. Queen’s University, Canada)

## Slide 17: Examples of clinical applications
Measurement of volumetric changes in slow growing meningioma

## Slide 18: Examples of clinical applications
Diffusion Tensor Imaging tractography for neurosurgical planning

## Slide 19: Overview
Part I: Introduction to the 3DSlicer software
Part II: 3D Data Loading and visualization of DICOM images
- Volume Rendering of thoraco-abdominal CT data
- Surface Rendering of MR head data
Part III: 3D interactive exploration of the anatomy
- Exploration of the Segments of the liver
- Exploration of the Segments of the lung

## Slide 20: Welcome to Slicer4
To start Slicer, double-click on the Slicer icon on the Desktop

## Slide 21: Navigating the Application GUI
The Graphic User Interface (GUI) of Slicer4 integrates four components:
the Menu Toolbar
the Module GUI Panel
the 3D Viewer
the Slice Viewer
Menu & Toolbar
Slice Viewers
3D Viewer
Module GUI Panel

## Slide 22: Welcome to Slicer4.3.1.1
Click on Welcome to Slicer to display the list of modules of Slicer in the Modules menu

## Slide 23: Welcome to Slicer4
Slicer4.3.1 contains more than 100 modules for image segmentation, registration and 3D visualization of medical imaging data

## Slide 24
Part 1:
Loading a DICOM Volume

## Slide 25: Tutorial datasets
The tutorial datasets are located in the Slicer Data directory on the Desktop, under
3DVisualizationDICOM_Tuesday_Dec3

## Slide 26: Loading a DICOM volume
Drag and drop the directory ‘dataset1_Thorax-Abdomen’ into Slicer

## Slide 27: Loading a DICOM volume
A pop-up window appears:
Select Load directory into DICOM database and click on OK

## Slide 28: Loading a DICOM volume
A pop-up window appears to notify the user that the DICOM database will be stored in a local directory
Click on OK

## Slide 29: Loading a DICOM volume
Slicer starts loading the DICOM images

## Slide 30: Loading a DICOM volume
Click on OK once the directory import is completed

## Slide 31: Loading a DICOM volume
The patient1 DICOM dataset appears in the DICOM browser.
Click on ‘patient1’ to display the file hierarchy, select the DICOM volume CT_Thorax_Abdomen_CT

## Slide 32: Loading a DICOM volume
Slicer displays the snapshots of the DICOM images of the CT_Thorax_Abdomen_CT dataset

## Slide 33: Loading a DICOM volume
Click on Load Selection to Slicer to load the DICOM volume into Slicer
(note: this may take a few minutes)

## Slide 34: Loading a DICOM volume
Slicer displays the axial, coronal and sagittal slices of the DICOM dataset

## Slide 35: Loading a DICOM volume
Select the Volumes module in the modules menu

## Slide 36: Loading a DICOM volume
Slicer has a series of window/level presets available
Click on the Window Level Preset CT-abdomen, or adjust manually the Window and Level using the Manual W/L slider
Select the Active Volume 6:CT_Thorax_Abdomen

## Slide 37: Loading a DICOM volume
Position the mouse cursor over the red banner in the Red Viewer to display the slice menu.
Click on the Links icon to link the slice controls across all Slice Viewers.
Click on the Eye icon to display the three anatomical slices in the 3D Viewer

## Slide 38: Loading a DICOM volume
The three anatomical slices appear in the 3D viewer. Use the right-mouse button in the 3D Viewer to zoom in and out

## Slide 39: Loading a DICOM volume
Use the left-mouse button in the 3D Viewer to rotate the 3D volume

## Slide 40: Loading a DICOM volume
Position the mouse over the blue banner in the 3D viewer window to display the 3DView controller, and click on the top left icon to center the 3D view on the scene
Note: a shortcut to this functionality is available through the icon next to the number ‘1’ in the blue banner

## Slide 41: Loading a DICOM volume
Click on the Slicer layout menu icon, and select the Conventional Widescreen layout

## Slide 42: Loading a DICOM volume
Use the red slice, yellow slice and green slice sliders to slice through the volume in all three anatomical directions

## Slide 43
3D Interactive exploration of thoraco-abdominal CT data using Volume Rendering

## Slide 44: Volume Rendering
Select the module Volume Rendering in the modules menu

## Slide 45: Volume Rendering
Select the volume 6:CT_Thorax_Abdomen

## Slide 46: Volume Rendering
Click on Preset in the Display tab to display the list of available presets for the transfer function
Select the Preset CT-Cardiac3

## Slide 47: Volume Rendering
Select the Rendering VTK CPU Ray Casting, and click on the eye icon in the Volume tab to display the Volume rendered volume in the 3D viewer

## Slide 48: Volume Rendering
Slicer displays the 3D rendered volume of the CT_Thorax_Abdomen dataset

## Slide 49: Volume Rendering
Move the Shift slider toward the right, to shift the transfer function and display the aorta

## Slide 50: Volume Rendering
The volume rendered image of the aorta and rib cage appears in the 3D viewer

## Slide 51: Volume Rendering
Click on the eye icon in the red viewer to turn off the visibility of the anatomical slices in the 3D viewer

## Slide 52: Volume Rendering
Use the mouse in the 3D window to rotate the volume rendered image

## Slide 53: Volume Rendering
Click on the eye icon in the volume rendering panel to remove the volume rendered image from the 3D viewer

## Slide 54: Volume Rendering
Click on Display ROI to display a region of interest that we will use for cropping the dataset, and check the option Enabled

## Slide 55: Volume Rendering
The region of interest appears in the 3DViewer

## Slide 56: Volume Rendering
Turn on the visibility of the grayscale images in to the 3D Viewer, and position the ROI around the left and right kidneys using the ROI controls in the 2D anatomical views and in the 3D viewer

## Slide 57: Volume Rendering
Click on the eye icon to display the volume rendered image of the kidney

## Slide 58: Volume Rendering
Slicer displays the volume rendered image of the left kidney

## Slide 59: Volume Rendering
Extend the ROI to the right kidney

## Slide 60: Volume Rendering
Slicer displays the cropped volume rendered images showing the left and right kidney

## Slide 61: Volume Rendering
Click on FileClose Scene to close the scene
Click on FileExit to quit Slicer

## Slide 62: Volume Rendering
Select Exit (discard modifications)

## Slide 63
3D visualization of surface models of the brain

## Slide 64: 3D Data Loading and Visualization
http://www.spl.harvard.edu/publications/item/view/2037
The dataset is composed of an MR scan of the brain and 3D surface reconstructions of anatomical structures.
The data are part of the SPL-PNL Brain Atlas developed by Talos, Jakab, Kikinis et al. The atlas is available at:

## Slide 65: 3D visualization of surface models of the brain : Viewing the Scene
Open the directory dataset2_Head located in
3DVisualizationDICOM_Tuesday_Dec3
Drag and drop the file Head_Scene.mrb into Slicer

## Slide 66: 3D visualization of surface models of the brain : Viewing the Scene
Click on OK to load the file MRHead_Scene.mrb into Slicer

## Slide 67: 3D visualization of surface models of the brain : Viewing the Scene
When the scene is finished loading, Slicer displays:
a 3D model of the head in the 3D Viewer, and
anatomical MR slices of the brain in the 2D Slice Viewers.
3D Viewer

## Slide 68: 3D visualization of surface models of the brain : Exploring Slicer’s functionality
To access the Models module, browse through the list of modules.

## Slide 69: 3D visualization of surface models of the brain : Switching to the Models Module
Slicer displays the GUI of the Models module.

## Slide 70: 3D visualization of surface models of the brain : Basic 3D Interaction
Position the mouse in the 3D Viewer.
Hold down the left mouse button and drag to rotate the model.
Left-click & drag

## Slide 71: 3D visualization of surface models of the brain : Viewing Slices in the 3D Viewer
Click on the Slice Visibility icon
to display the Axial Slice in the 3D Viewer

## Slide 72: 3D visualization of surface models of the brain
Slicer adds a view of the Axial slice in the 3D View.

## Slide 73: 3D visualization of surface models of the brain : Viewing Slices in the 3D Viewer
Click on the layout menu in the toolbar, and select the Conventional layout

## Slide 74: 3D visualization of surface models of the brain
Select the Skin.vtk
Change the opacity of the model from 1.0 to 0.0.

## Slide 75: 3D visualization of surface models of the brain
skin model opacity = 0.5

## Slide 76: 3D visualization of surface models of the brain
The model of the skin becomes invisible in the 3D viewer.
(skin model opacity = 0.0)

## Slide 77: 3D visualization of surface models of the brain
Click on the Slice Visibility icon in the Green Slice Viewer
to display the Coronal Slice in the 3D Viewer.

## Slide 78: 3D visualization of surface models of the brain
The Axial and Coronal Slices are displayed in the 3D Viewer.

## Slide 79: 3D visualization of surface models of the brain
Select the 3D model skull_bone.vtk in the Model Hierarchy and turn on the Clipping option.

## Slide 80: 3D visualization of surface models of the brain
Browse through the coronal slices to expose the 3D model of the white matter, and the left and right optic nerves.

## Slide 81: 3D visualization of surface models of the brain
Now make the skull invisible.

## Slide 82: 3D visualization of surface models of the brain
Scroll the Coronal Slices to display the hemispheric white matter model in the context of the image data in the 3D Viewer.

## Slide 83: 3D visualization of surface models of the brain
Select the hemispheric white matter model called
hemispheric_white_matter.vtk
Turn off its visibility.

## Slide 84: 3D visualization of surface models of the brain
Slicer displays the optic nerve, optic chiasm and optic tracts overlaid on the MR images of the brain.

## Slide 85: 3D visualization of surface models of the brain
Windows/Linux users: Position the mouse in the 3D Viewer, hold down the right mouse button and move the mouse down to zoom in.
Mac users: Position the mouse in the 3D Viewer, hold down the apple button and the mouse button and move the mouse down to zoom in
(or use two fingers on the touch pad).

## Slide 86: 3D visualization of surface models of the brain
Slicer displays a closer view of 3D anatomical structures overlaid on 2D MR slices

## Slide 87: Close the existing scene and all its data
Select File->Close Scene
This removes any dataset previously loaded into Slicer.
Select FileExit to exit the software

## Slide 88: Overview
Part I: Introduction to the 3DSlicer software
Part II: 3D Data Loading and visualization of DICOM images
- Volume Rendering of thoraco-abdominal CT data
- Surface Rendering of MR head data
Part III: 3D interactive exploration of the anatomy
- Exploration of the Segments of the liver
- Exploration of the Segments of the lung

## Slide 89: Slicer for Radiology Education
Models completed as ‘virtual dissection’ by a medical student who is now a radiology resident

## Slide 90
Part II:
Interactive 3D Visualization of the segments of the liver

## Slide 91: Anatomy of the liver

## Slide 92: Liver dataset
The liver dataset is
a contrast-enhanced CT
abdominal scan of a
healthy 36 year-old male.

## Slide 93: 3D segments of the liver
Segment II
Segment III
Segment IVa
Segment IVb
Segment VI
Segment V
Segment VII

## Slide 94: 3D segments of the liver
Segment II
Segment V
Segment VII
Segment I
IVC
Segment VI
Segment III
Segment IVb

## Slide 95: Liver vasculature
Caudate vein
Main portal vein
Left portal vein
IVC
Right hepatic vein
Left hepatic vein
Right portal vein
Middle hepatic vein

## Slide 96: Loading the Liver Scene
Browse to the directory 3DVisualizationDICOM_Tuesday_Dec3
Select the directory dataset3_Liver
Drag and drop the file LiverSegments_Scene.mrb into Slicer
Click on OK to load the scene into Slicer

## Slide 97: Loading the Liver Scene
Click on OK to load the scene into Slicer

## Slide 98: Liver Segments Scene
The elements of the scene appear in the Viewer

## Slide 99: 3D models of the liver
Segment II
Segment III
Segment IVa
Segment IVb
Segment VI
Segment V
Segment VIII
Segment VII

## Slide 100: 3D models of the liver
Segment II
Segment V
Segment VII
Segment I
IVC
Segment VI
Segment III
Segment IVb

## Slide 101: 3D models of the liver
Caudate vein
Main portal vein
Left portal vein
IVC
Right hepatic vein
Left hepatic vein
Right portal vein
Middle hepatic vein

## Slide 102: 3D Exploration of Liver Segments
Example:
What organ abuts the
left-most margin of
segment II in this
patient ?
Notes: 102

## Slide 103: 3D Exploration of Liver Segments
Select the module Models
Click on the Liver Structures Models Hierarchy
Notes: 103

## Slide 104: 3D Exploration of Liver Segments
Select the model Liver_Segment II
Turn on/off its visibility to locate
it in the 3D viewer.
Notes: 104

## Slide 105
Position the mouse in the 3D Viewer, hold down the left mouse button and drag to orient the 3D model to a superior view.
National Alliance for Medical Image Computing
http://na-mic.org © 2010, ARR
3D Exploration of Liver Segments
Notes: 105

## Slide 106
Seg II
Question 1:
What organ abuts the left-most margin of segment II in Patient 1?
3D Exploration of Liver Segments
Notes: 106
106

## Slide 107
stomach
Seg II
Question 1:
What organ abuts the left-most margin of segment II in this patient?
Answer 1: Stomach
3D Exploration of Liver Segments
Notes: 107
107

## Slide 108
Question 2:
Which segment would
most likely be affected by
an aggressive tumor
invading locally from the
right adrenal gland ?
3D Exploration of Liver Segments
Notes: 108

## Slide 109
Segment VII
Question 2:
Which segment would
most likely be affected by
an aggressive tumor
invading locally from the
right adrenal gland ?
Answer 2: Segment VII
3D Exploration of Liver Segments
Notes: 109

## Slide 110
Question 3:
Which vessel separates Segment IVb and Segment V?
3D Exploration of Liver Segments
Notes: 110

## Slide 111: Middle Hepatic Vein
Segment V
Segment IVb
Question 3:
Which vessel separates Segment IVb and Segment V?
Answer 3: The middle hepatic vein
Middle hepatic vein
Notes: 111

## Slide 112: Closing the Liver Scene
Select File  Close Scene and FileExit

## Slide 113
Interactive 3D Visualization of the segments of the lungs

## Slide 114: Segments of the lung
Segmentation and 3D surface reconstruction of the lung and pulmonary vessels

## Slide 115: Segments of the lung
3D parcellation of arteries and veins from original model of pulmonary vessels
Right Upper Lobe (RUL)
  RUL Pulmonary Vein
  RUL Anterior Segment
  RUL Apical Segment
  RUL Posterior Segment
Right Middle Lobe (RML)
  RML Pulmonary Vein 1 & 2
  RML Lateral Segment
  RML Medial Segment
Right Lower Lobe (RLL)
  RLL Pulmonary Vein 1,2,3
  RLL Anterior Basal Segment
  RLL Medial Basal Segment
  RLL Lateral Basal Segment
  RLL Posterior Basal Segment

## Slide 116: Loading the Chest Data Scene
3DVisualizationDICOM_Tuesday_Dec3
Select the subdirectory dataset4_Chest
Drag and drop the file LungSegments_Scene.mrb into Slicer

## Slide 117: Loading the Lung Scene
Click on OK to load the file into Slicer

## Slide 118: Loading the Lung Scene

## Slide 119
Loading the Lung Scene
Select the module Models from the modules Menu.

## Slide 120: Lung Segments
Slicer displays the list of 15 surface models of pulmonary structures.

## Slide 121: Lung Segments – Question 1
Q1: Why is there a gap in the vessels at the arrows?

## Slide 122: Lung Segments – Answer 1
A1: Major fissure

## Slide 123: Lung Segments – Question 2
Q2. Which segment would be most likely to be the source of bleeding from a depressed right clavicle fracture?

## Slide 124: Lung Segments – Answer 2
RUL-Apical
RUL-Posterior

## Slide 125: Lung Segments – Question 3
Q3: Which lower lobe segment would likely be involved by a tumor growing downward from the right middle lobe medial segment?

## Slide 126: Lung Segments – Answer 3
A3: Anterior Basal
RML-medial
RLL-anterior basal

## Slide 127: Lung Segments – Question 4
Question 4: Classify the segments of the lower lobe by size

## Slide 128: Lung Segments – Question 4
A4: Smallest: Medial Basal

## Slide 129: Lung Segments – Question 4
A4: Largest: Anterior / Posterior Basal

## Slide 130: 3D Visualization of DICOM images
Interactive user-interface to load and manipulate greyscale volumes, labelmaps and 3D models.
User-defined 3D view of the anatomy
3D Open-source platform for Linux, Mac and Windows

## Slide 131: 3DSlicer website

## Slide 132: www.slicer.org

## Slide 133: 3DSlicer at RSNA 2013
  Quantitative Imaging Reading Room Exhibit
  QIRR 1028, Lakeside Center
Daily meet the experts session, 12:15-1:15 pm
3DSlicer: An Open Source Platform for Segmentation, Registration, Quantitative Imaging, and 3D Visualization of Multi-Modal Image Data.
Sonia Pujol, PhD, Steve Pieper, PhD, Andriy Fedorov, PhD, Ron Kikinis, MD,

## Slide 134: Additional Related Hands-on courses
  Wed 10:30 am – Open Access Imaging Data Resources: NIH Cancer Imaging Archive (ICIA41)
  Wed 12:30 pm – Correlating Imaging with Human Genomics (ICIA42)
All courses are in this Advanced Imaging Classroom: S401CD

## Slide 135: 3DSlicer at RSNA
Questions: spujol@bwh.harvard.edu

## Slide 136: Acknowledgments
National Alliance for Medical Image Computing (NA-MIC)
(NIH Grant U54EB005149)
Neuroimage Analysis Center (NAC)
(NIH Grant P41 RR013218)
Marianna Jakab, Surgical Planning Laboratory, Brigham
and Women’s Hospital

## Slide 137
www.slicer.org
www.na-mic.org
Questions and comments: spujol@bwh.harvard.edu